## Slide 1: Mechanical
Essentially windvanes, using a pivoting, overstable wing to determine current direction
Sense speed using a rotor that is spun by the current
Mechanically very simple
Creates more points of failure
Very achievable to manufacture
Likely to be the first component on PUCKfish to fail

## Slide 2: IMU
IMU returns approximation of current based on puck’s movement on a cable
Simplest possible implementation mechanically
Gives relatively poor accuracy for current speed
Would need to derive relationship between puck movement and current

## Slide 3: Acoustic Doppler Sensors
Device emits low frequency sound, which then scatters in the water.
Several microphones use both the return frequency and time difference between microphones to determine current speed and direction
State of the art
  Most accurate
  Most expensive
Complicated to design and manufacture in house
Expensive to purchase COTS

## Slide 4: EM Sensing
An inductor, exposed to the current, generates an oscillating magnetic field
A voltage is induced by the moving seawater within the inductor
This oscillating voltage is then measured, giving the current speed in the direction of the induced magnetic field
Mechanically extremely simple
Could give direction with the addition of a second, perpendicular inductor
Unclear what magnitude the voltage changes will be
Potentially difficult to model
Could require greater power draw than other alternatives, due to the magnetic field

## Slide 5: Source
Williams, Albert. Current Measurement Technology Committee of the Oceanic Engineering Society of IEEE. 1/1/08. https://www.hydro-international.com/content/article/ocean-current-measurements-a-review.